## Slide 1: Practical Assurance Case Design
IV&V Workshop
S. R. Brown
KeyLogic Inc
With my thanks and appreciation
Don Ohi – Project Monitor
Travis Dawson – Chief Engineer
Bill Stanton for tolerating a lot of questions

## Slide 2: Why Assurance Cases
State your case:
  What are we trying to prove
  How are we trying to prove it
  What evidence supports the proof
Assurance Cases make the point
Design of Assurance
Support of Assurance
Related to:
Argumentation
Safety Case
GSN Standard Kelly, T.: 'Arguing Safety: A Systematic Approach to Managing Safety Cases', D.Phil Thesis, University of York (1998). Available for download from http://www-users.cs.york.ac.uk/~tpk

## Slide 3: State Your Case
Spousal Coffee Assurance Case
Top level Claim
Claim Justification
Perspective: Who is the stakeholder?

## Slide 4: Make the Argument
Architectural decomposition
Behavioral decomposition

## Slide 5: Gather the Evidence
Atomic evidence

## Slide 6: Assurance Case Semantic Content
What I get out of a cup of coffee:
  The assurance design is not a description of the system
  Assurance network needs only to go as far as necessary to provide stated assurance
  Strength of evidence is a constant consideration
  Without more information there is little basis for claim prioritization
    Can address risk (uncertainty)
    Does not support consequence

## Slide 7: Where to Start
Testable (yes/no)
Is Clearly Stated
Will decompose in a useful way
Lessons Learned:
Look for simple and comprehensive claims
Claims must be objective (yes/no)
Watch out for claims that must decompose through out-of-scope domains (e.g.: reset/sideswap hardware timing)
Take advantage of self-similarity, patterns and common arguments.
Initially a major goal: In almost every case it is self-evident if the objective is defined. This is where perspective becomes important. Consider stakeholder needs.

## Slide 8: Perspectives and Planning
The perspective of the assurance case is important
  Software lifecycle (NPR 7150)
  System/Human safety
  09-1 System definition
  Project-specific
A place for (almost) everything
Decomposes differently than lifecycle
Represent the stakeholder

## Slide 9: Argument: the Art of Assurance Case
Some Useful decomposition classes
Appeal to architecture
Use software architecture to decompose to subsystems
No uncertainty
Appeal to Usage
Use scenario to decompose to subsystems by required actions
Some uncertainty
Note: 3Q is a special case of appeal to usage
Appeal to Specificity
Provide detail to support a more general claim
Little uncertainty
Arguments describe how the child claims satisfy the parent claim but do not carry the burden of proof
Some approaches require a justification for each argument but this was often redundant.
Assumptions are often necessary in order that the argument is clear to a reviewer
Arguments are in the context of the system
Use cases can be a good basis for an Appeal to Usage. Note semantic equivalence.

## Slide 10: When to Stop
Completeness
  Are all claims fully decomposed?
  Are all assumptions described?
Depth
  Is there evidence that is directly relatable?
Abstraction
  Are sub-claims at (more or less) the same level of abstraction?
  Is evidence ascribed at the appropriate level of abstraction?
Generally the lowest level claim can be supported by one or more low level requirements.
  Software architecture level
  System-level tests and requirements are evidence too, but lower-level evidence is earlier in the project and often less ambiguous.

## Slide 11: Top Down or Bottom Up?
GSN Standard describes both methods, then tosses in a third – use both.
Practical use dictates that both are necessary for IV&V
  Top level claims provide the entire motivation for the assurance case
  Evidence is determined by a combination of artifacts and IV&V analysis.

## Slide 12: GENERIC PBRA Summary
GENERIC PBRA Summary
GNC Driver

## Slide 13: Using the Assurance Cases with PBRA
We can map scenario steps to the assurance case because we used them for decomposition
Semantically, it seems that scenarios map to arguments (decomp by behavior), and scenario steps map to claims.

## Slide 14: Odd topics
Where does static code analysis fit into the picture?
  Certainly provides assurance in some sense
  Applies to the product in general but traceable to architectural components
  Claim: “Module XYZ is free of implementation flaws”
How does uncertainty fit into the picture?
  IEEE15026 assumes there is a way to combine the independent (and ill-defined) components of uncertainty, or at least specify uncertainty.
  Even if we could calculate uncertainty, would it be a Good Thing? Would broad categories be sufficient?

## Slide 15: And now for something you will really like
Hot spots for development
  Algorithmic blind spots
  Scoring or ranking system
  Real project testbed
Is a practical S/C assurance case possible?
Is a practical S/C assurance case useful?
Is it difficult to write top-level claims?
Is it difficult to develop arguments for decomposition?
Can this be a uniform and systematic process for each project?
Yes
Yes – if well-designed
Not at all
Only in a few cases
Structured GSN
Re-usability of assurance design